## Slide 1: CS162 Operating Systems and Systems Programming Lecture 3 Processes (con’t), System Calls, Fork,
January 25th, 2022
Prof. Anthony Joseph and John Kubiatowicz
http://cs162.eecs.Berkeley.edu

## Slide 2: Recall: Four Fundamental OS Concepts
Thread: Execution Context
  Fully describes program state
  Program Counter, Registers, Execution Flags, Stack
Address space (with or w/o translation)
  Set of memory addresses accessible to program (for read or write)
  May be distinct from memory space of the physical machine (in which case programs operate in a virtual address space)
Process: an instance of a running program
  Protected Address Space + One or more Threads
Dual mode operation / Protection
  Only the “system” has the ability to access certain resources
  Combined with translation, isolates programs from each other and the OS from programs

## Slide 3: Recall: OS Bottom Line: Run Programs
int main()
{ … ;
}
editor
Program Source
foo.c
Load & Execute
Memory
PC:
Processor
registers
0x000…
0xFFF…
instructions
data
heap
stack
OS
compiler
Executable
a.out
data
instructions
Create OS “PCB”, address space, stack and heap
Load instruction and data segments of executable file into memory
“Transfer control to program”
Provide services to program
While protecting OS and program

## Slide 4: Recall: Protected Address Space
Program operates in an address space that is distinct from the physical memory space of the machine
Processor
Memory
0x000…
0xFFF…
translator
“virtual address”
“physical address”
Registers
Page Table
<Frame Addr>

## Slide 5: Recall: Single and Multithreaded Processes
Threads encapsulate concurrency: “Active” component
Address spaces encapsulate protection: “Passive” part
  Keeps buggy program from trashing the system
Why have multiple threads per address space?
Notes: Sometimes need parallelism for a single job, and processes are very expensive – to start, switch between, and to communicate between

## Slide 6: Recall: Simple address translation with Base and Bound
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack
0000…
FFFF…
1000…
0000…
Program
address
Base Address
Bound
<
1000…
1100…
0100…
Can the program touch OS?
Can it touch other programs?
0010…
0010…
Addresses translated on-the-fly
1010…
0100…

## Slide 7: Simple B&B: User => Kernel
OS
Proc 1
Proc 2
Proc n
…
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack
0000…
FFFF…
1000…
1100…
3000…
3080…
Base
1000 …
1100…
Bound
xxxx…
uPC
regs
sysmode
…
0
PC
0000…
FFFF…
00FF…
How to return to system?
0000 1234

## Slide 8: Simple B&B: Interrupt
OS
Proc 1
Proc 2
Proc n
…
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack
0000…
FFFF…
1000…
1100…
3000…
3080…
Base
1000 …
1100 …
Bound
0000 1234
uPC
regs
sysmode
…
1
PC
0000…
FFFF…
00FF…
How to save registers and set up system stack?
IntrpVector[i]

## Slide 9: Simple B&B: Switch User Process
OS
Proc 1
Proc 2
Proc n
…
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack
0000…
FFFF…
1000…
1100…
3000…
3080…
Base
3000 …
0080 …
Bound
0000 0248
uPC
regs
sysmode
…
1
PC
0000…
FFFF…
00D0…
How to save registers and set up system stack?
0001 0124
1000 …
1100 …
0000 1234
regs
00FF…
RTU

## Slide 10: Simple B&B: “resume”
OS
Proc 1
Proc 2
Proc n
…
code
Static Data
heap
stack
code
Static Data
heap
stack
code
Static Data
heap
stack
0000…
FFFF…
1000…
1100…
3000…
3080…
Base
3000 …
0080 …
Bound
xxxx xxxx
uPC
regs
sysmode
…
0
PC
0000…
FFFF…
00D0…
How to save registers and set up system stack?
000 0248
1000 …
1100 …
0000 1234
regs
00FF…
RTU

## Slide 11: Running Many Programs
We have the basic mechanism to
  switch between user processes and the kernel,
  the kernel can switch among user processes,
  Protect OS from user processes and processes from each other
Questions ???
  How do we represent user processes in the OS?
  How do we decide which user process to run?
  How do we pack up the process and set it aside?
  How do we get a stack and heap for the kernel?
  Aren’t we wasting are lot of memory?

## Slide 12: Multiplexing Processes: The Process Control Block
Kernel represents each process as a process control block (PCB)
  Status (running, ready, blocked, …)
  Register state (when not ready)
  Process ID (PID), User, Executable, Priority, …
  Execution time, …
  Memory space, translation, …
Kernel Scheduler maintains a data structure containing the PCBs
  Give out CPU to different processes
  This is a Policy Decision
Give out non-CPU resources
  Memory/IO
  Another policy decision
Process Control
Block

## Slide 13: CPU Switch From Process A to Process B
Kernel/System Mode
User Mode
User Mode

## Slide 14: Scheduler
Scheduling: Mechanism for deciding which processes/threads receive the CPU
Lots of different scheduling policies provide …
  Fairness or
  Realtime guarantees or
  Latency optimization or ..
if ( readyProcesses(PCBs) ) {
nextPCB = selectProcess(PCBs);
run( nextPCB );
} else {
run_idle_process();
}

## Slide 15: Simultaneous MultiThreading/Hyperthreading
Hardware scheduling technique
  Superscalar processors can execute multiple instructions that are independent.
  Hyperthreading duplicates register state to make a second “thread,” allowing more instructions to run.
Can schedule each thread as if were separate CPU
  But, sub-linear speedup!
Original technique called “Simultaneous Multithreading”
  http://www.cs.washington.edu/research/smt/index.html
  SPARC, Pentium 4/Xeon (“Hyperthreading”), Power 5
Colored blocks show
instructions executed
Notes: Intel seems to be discarding SMT in Silvermont because of power problems

## Slide 16: Also recall: The World Is Parallel: Intel SkyLake (2017)
Up to 28 Cores, 56 Threads
  694 mm² die size (estimated)
Many different instructions
  Security, Graphics
Caches on chip:
  L2: 28 MiB
  Shared L3: 38.5 MiB (non-inclusive)
  Directory-based cache coherence
Network:
  On-chip Mesh Interconnect
  Fast off-chip network directlry supports 8-chips connected
DRAM/chips
  Up to 1.5 TiB
  DDR4 memory

## Slide 17: Is Base and Bound a Good-Enough Protection Mechanism?
NO: Too simplistic for real systems
Inflexible/Wasteful:
  Must dedicate physical memory for potential future use
  (Think stack and heap!)
Fragmentation:
  Kernel has to somehow fit whole processes into contiguous block of memory
  After a while, memory becomes fragmented!
Sharing:
  Very hard to share any data between Processes or between Process and Kernel
  Need to communicate indirectly through the kernel…

## Slide 18: Better: x86 – segments and stacks
CS
EIP
SS
ESP
DS
ECX
ES
EDX
ESI
EDI
EAX
EBX
code
Static Data
heap
stack
code
Static Data
heap
stack
CS:
EIP:
SS:
ESP:
Processor Registers
Start address, length and access rights associated with each segment

## Slide 19: Better Alternative: Address Mapping
Prog 1
Virtual
Address
Space 1
Prog 2
Virtual
Address
Space 2
Code
Data
Heap
Stack
Code
Data
Heap
Stack
Data 2
Stack 1
Heap 1
OS heap &
Stacks
Code 1
Stack 2
Data 1
Heap 2
Code 2
OS code
OS data
Translation Map 1
Translation Map 2
Physical Address Space

## Slide 20: Administrivia: Getting started!
Kubiatowicz Office Hours:
  1-2pm, Monday & Thursday
Homework 0 Due Tomorrow!
  Get familiar with the cs162 tools
  configure your VM, submit via git
  Practice finding out information:
    How to use GDB? How to understand output of unix tools?
    We don’t assume that you already know everything!
    Learn to use “man” (command line), “help” (in gdb, etc), google
Should be going to sections now – Important information there
  Any section will do until groups assigned
THIS Friday is Drop Deadline! HARD TO DROP LATER!
  If you know you are going to drop, do so now to leave room for others on waitlist!
  Why do we do this? So that groups aren’t left without members!

## Slide 21: Administrivia (Con’t)
Group sign up via autograder form next week
  Get finding groups of 4 people ASAP
  Priority for same section; if cannot make this work, keep same TA
  Remember: Your TA needs to see you in section!
Midterm 1: 2/17
  7-9PM in person
  We will say more about material when we get closer…
Midterm 1 conflicts
  We will handle these conflicts after have final class roster
  Watch for queries by HeadTA to collect information

## Slide 22: Recall: 3 types of Kernel Mode Transfer
Syscall
  Process requests a system service, e.g., exit
  Like a function call, but “outside” the process
  Does not have the address of the system function to call
  Like a Remote Procedure Call (RPC) – for later
  Marshall the syscall id and args in registers and exec syscall
Interrupt
  External asynchronous event triggers context switch
  eg. Timer, I/O device
  Independent of user process
Trap or Exception
  Internal synchronous event in process triggers context switch
  e.g., Protection violation (segmentation fault), Divide by zero, …

## Slide 23: Recall: User/Kernel (Privileged) Mode
User Mode
Kernel Mode
Full HW access
Limited HW access
exec
syscall
exit
rtn
interrupt
rfi
exception

## Slide 24: Implementing Safe Kernel Mode Transfers
Important aspects:
  Controlled transfer into kernel (e.g., syscall table)
  Separate kernel stack!
Carefully constructed kernel code packs up the user process state and sets it aside
  Details depend on the machine architecture
  More on this next time
Should be impossible for buggy or malicious user program to cause the kernel to corrupt itself!

## Slide 25: Hardware support: Interrupt Control
Interrupt processing not visible to the user process:
  Occurs between instructions, restarted transparently
  No change to process state
  What can be observed even with perfect interrupt processing?
Interrupt Handler invoked with interrupts ‘disabled’
  Re-enabled upon completion
  Non-blocking (run to completion, no waits)
  Pack up in a queue and pass off to an OS thread for hard work
    wake up an existing OS thread

## Slide 26: Interrupt Controller
Interrupts invoked with interrupt lines from devices
Interrupt controller chooses interrupt request to honor
  Interrupt identity specified with ID line
  Mask enables/disables interrupts
  Priority encoder picks highest enabled interrupt
  Software Interrupt Set/Cleared by Software
CPU can disable all interrupts with internal flag
Non-Maskable Interrupt line (NMI) can’t be disabled
Network
IntID
Interrupt
Interrupt Mask
Control
Software
Interrupt
NMI
CPU
Priority Encoder
Timer
Int Disable

## Slide 27: Interrupt Vector
Where else do you see this dispatch pattern?
  System Call
  Exceptions
interrupt number (i)
intrpHandler_i () {
….
}
Address and properties of each interrupt handler

## Slide 28: How do we take interrupts safely?
Interrupt vector
  Limited number of entry points into kernel
Kernel interrupt stack
  Handler works regardless of state of user code
Interrupt masking
  Handler is non-blocking
Atomic transfer of control
  “Single instruction”-like to change:
    Program counter
    Stack pointer
    Memory protection
    Kernel/user mode
Transparent restartable execution
  User program does not know interrupt occurred

## Slide 29: Need for Separate Kernel Stacks
Kernel needs space to work
Cannot put anything on the user stack (Why?)
Two-stack model
  OS thread has interrupt stack (located in kernel memory) plus User stack (located in user memory)
  Syscall handler copies user args to kernel space before invoking specific function (e.g., open)
  Interrupts (???)

## Slide 30: Before

## Slide 31: During Interrupt/System Call

## Slide 32: Recall: UNIX System Structure
User Mode
Kernel Mode
Hardware
Applications
Standard Libs

## Slide 33: A Narrow Waist
Compilers
Web Servers
Web Browsers
Databases
Email
Word Processing
Portable OS Library
System Call
Interface
Portable OS Kernel
Platform support, Device Drivers
x86
ARM
PowerPC
Ethernet (1Gbs/10Gbs)
802.11 a/g/n/ac/ax
SCSI
Thunderbolt
Graphics
PCI
Hardware
Software
System Mode
User Mode
OS
Application / Service

## Slide 34: Kernel System Call Handler
Vector through well-defined syscall entry points!
  Table mapping system call number to handler
Locate arguments
  In registers or on user (!) stack
Copy arguments
  From user memory into kernel memory
  Protect kernel from malicious code evading checks
Validate arguments
  Protect kernel from errors in user code
Copy results back
  Into user memory

## Slide 35: Putting it together: web server
Request
Reply
(retrieved by web server)
Client
Web Server

## Slide 36: Putting it together: web server
Server Process
Kernel
Hardware
request
buffer
reply
buffer
11. kernel copy
from user buffer
to network buffer
Network
interface
Disk interface
12. format outgoing
packet and DMA
6. disk
request
network
socket
read()
2. copy arriving
packet (DMA)
syscall
wait
interrupt
3. kernel
copy
RTU
5. file
read()
syscall
8. kernel
copy
RTU
7. disk data
(DMA)
interrupt
4. parse request
9. format reply
Request
Reply
10. network
socket
write()
syscall
wait

## Slide 37: Recall: Processes
How to manage process state?
  How to create a process?
  How to exit from a process?
Remember: Everything outside of the kernel is running in a process!
  Including the shell! (Homework 2)
Processes are created and managed… by processes!

## Slide 38: Bootstrapping
If processes are created by other processes, how does the first process start?
First process is started by the kernel
  Often configured as an argument to the kernel before the kernel boots
  Often called the “init” process
After this, all processes on the system are created by other processes

## Slide 39: Process Management API
exit – terminate a process
fork – copy the current process
exec – change the program being run by the current process
wait – wait for a process to finish
kill – send a signal (interrupt-like notification) to another process
sigaction – set handlers for signals

## Slide 40: Process Management API
exit – terminate a process
fork – copy the current process
exec – change the program being run by the current process
wait – wait for a process to finish
kill – send a signal (interrupt-like notification) to another process
sigaction – set handlers for signals

## Slide 41: pid.c
#include <stdlib.h>
#include <stdio.h>
#include <string.h>
#include <unistd.h>
#include <sys/types.h>
int main(int argc, char *argv[])
{
/* get current processes PID */
pid_t pid = getpid();
printf("My pid: %d\n", pid);
exit(0);
}
Q: What if we let main return without ever calling exit?
The OS Library calls exit() for us!
The entrypoint of the executable is in the OS library
OS library calls main
If main returns, OS library calls exit
You’ll see this in Project 0: init.c

## Slide 42: Process Management API
exit – terminate a process
fork – copy the current process
exec – change the program being run by the current process
wait – wait for a process to finish
kill – send a signal (interrupt-like notification) to another process
sigaction – set handlers for signals

## Slide 43: Creating Processes
pid_t fork() – copy the current process
  New process has different pid
  New process contains a single thread
Return value from fork(): pid (like an integer)
  When > 0:
    Running in (original) Parent process
    return value is pid of new child
  When = 0:
    Running in new Child process
  When < 0:
    Error! Must handle somehow
    Running in original process
State of original process duplicated in both Parent and Child!
  Address Space (Memory), File Descriptors (covered later), etc…

## Slide 44: fork1.c
#include <stdlib.h>
#include <stdio.h>
#include <unistd.h>
#include <sys/types.h>
int main(int argc, char *argv[]) {
pid_t cpid, mypid;
pid_t pid = getpid(); /* get current processes PID */
printf("Parent pid: %d\n", pid);
cpid = fork();
if (cpid > 0) { /* Parent Process */
mypid = getpid();
printf("[%d] parent of [%d]\n", mypid, cpid);
} else if (cpid == 0) { /* Child Process */
mypid = getpid();
printf("[%d] child\n", mypid);
} else {
perror("Fork failed");
}
}

## Slide 45: fork1.c
#include <stdlib.h>
#include <stdio.h>
#include <unistd.h>
#include <sys/types.h>
int main(int argc, char *argv[]) {
pid_t cpid, mypid;
pid_t pid = getpid(); /* get current processes PID */
printf("Parent pid: %d\n", pid);
cpid = fork();
if (cpid > 0) { /* Parent Process */
mypid = getpid();
printf("[%d] parent of [%d]\n", mypid, cpid);
} else if (cpid == 0) { /* Child Process */
mypid = getpid();
printf("[%d] child\n", mypid);
} else {
perror("Fork failed");
}
}
p
c

## Slide 46: fork1.c
#include <stdlib.h>
#include <stdio.h>
#include <unistd.h>
#include <sys/types.h>
int main(int argc, char *argv[]) {
pid_t cpid, mypid;
pid_t pid = getpid(); /* get current processes PID */
printf("Parent pid: %d\n", pid);
cpid = fork();
if (cpid > 0) { /* Parent Process */
mypid = getpid();
printf("[%d] parent of [%d]\n", mypid, cpid);
} else if (cpid == 0) { /* Child Process */
mypid = getpid();
printf("[%d] child\n", mypid);
} else {
perror("Fork failed");
}
}
p
c

## Slide 47: fork_race.c
int i;
pid_t cpid = fork();
if (cpid > 0) {
for (i = 0; i < 10; i++) {
printf("Parent: %d\n", i);
// sleep(1);
}
} else if (cpid == 0) {
for (i = 0; i > -10; i--) {
printf("Child: %d\n", i);
// sleep(1);
}
}
What does this print?
Would adding the calls to sleep() matter?
Recall: a process consists of one or more threads executing in an address space
Here, each process has a single thread
These threads execute concurrently

## Slide 48: Running Another Program
With threads, we could call pthread_create to create a new thread executing a separate function
With processes, the equivalent would be spawning a new process executing a different program
How can we do this?

## Slide 49: Process Management API
exit – terminate a process
fork – copy the current process
exec – change the program being run by the current process
wait – wait for a process to finish
kill – send a signal (interrupt-like notification) to another process
sigaction – set handlers for signals

## Slide 50: fork3.c
…
cpid = fork();
if (cpid > 0) { /* Parent Process */
tcpid = wait(&status);
} else if (cpid == 0) { /* Child Process */
char *args[] = {“ls”, “-l”, NULL};
execv(“/bin/ls”, args);
/* execv doesn’t return when it works.
So, if we got here, it failed! */
perror(“execv”);
exit(1);
}
…

## Slide 51: Process Management
main() {
…
}
pid=fork();
if (pid==0)
exec(…);
else
wait(&stat)
child
parent
pid=fork();
if (pid==0)
exec(…);
else
wait(&stat)
pid=fork();
if (pid==0)
exec(…);
else
wait(&stat)
fork
fork
wait
exec

## Slide 52: Process Management API
exit – terminate a process
fork – copy the current process
exec – change the program being run by the current process
wait – wait for a process to finish
kill – send a signal (interrupt-like notification) to another process
sigaction – set handlers for signals

## Slide 53: fork2.c – parent waits for child to finish
int status;
pid_t tcpid;
…
cpid = fork();
if (cpid > 0) { /* Parent Process */
mypid = getpid();
printf("[%d] parent of [%d]\n", mypid, cpid);
tcpid = wait(&status);
printf("[%d] bye %d(%d)\n", mypid, tcpid, status);
} else if (cpid == 0) { /* Child Process */
mypid = getpid();
printf("[%d] child\n", mypid);
exit(42);
}
…

## Slide 54: Process Management API
exit – terminate a process
fork – copy the current process
exec – change the program being run by the current process
wait – wait for a process to finish
kill – send a signal (interrupt-like notification) to another process
sigaction – set handlers for signals

## Slide 55: inf_loop.c
#include <stdlib.h>
#include <stdio.h>
#include <sys/types.h>
#include <unistd.h>
#include <signal.h>
void signal_callback_handler(int signum) {
printf(“Caught signal!\n”);
exit(1);
}
int main() {
struct sigaction sa;
sa.sa_flags = 0;
sigemptyset(&sa.sa_mask);
sa.sa_handler = signal_callback_handler;
sigaction(SIGINT, &sa, NULL);
while (1) {}
}
Q: What would happen if the process receives a SIGINT signal, but does not register a signal handler?
A: The process dies!
For each signal, there is a default handler defined by the system

## Slide 56: Common POSIX Signals
SIGINT – control-C
SIGTERM – default for kill shell command
SIGSTP – control-Z (default action: stop process)
SIGKILL, SIGSTOP – terminate/stop process
  Can’t be changed with sigaction
  Why?

## Slide 57: Shell
A shell is a job control system
  Allows programmer to create and manage a set of programs to do some task
You will build your own shell in Homework 2…
  … using fork and exec system calls to create new processes…
  … and the File I/O system calls we’ll see next time to link them together

## Slide 58: Process vs. Thread APIs
Why have fork() and exec() system calls for processes, but just a pthread_create() function for threads?
  Convenient to fork without exec: put code for parent and child in one executable instead of multiple
  It will allow us to programmatically control child process’ state
    By executing code before calling exec() in the child
  We’ll see this in the case of File I/O next time
Windows uses CreateProcess() instead of fork()
  Also works, but a more complicated interface

## Slide 59: Threads vs. Processes
If we have two tasks to run concurrently, do we run them in separate threads, or do we run them in separate processes?
Depends on how much isolation we want
  Threads are lighter weight [why?]
  Processes are more strongly isolated

## Slide 60: Conclusion
Process: execution environment with Restricted Rights
  Address Space with One or More Threads
  Owns memory (address space)
  Owns file descriptors, file system context, …
  Encapsulate one or more threads sharing process resources
Interrupts
  Hardware mechanism for regaining control from user
  Notification that events have occurred
  User-level equivalent: Signals
Native control of Process
  Fork, Exec, Wait, Signal